## Slide 1
WattWise
An Intelligent Home Energy Management and Monitoring System
TEAMWORK

## Slide 2
Rising Costs & Tier Tariffs
Egyptian households face tier-based electricity tariffs and prepaid meters without clear visibility of consumption breakdown.
Lack of Appliance Visibility
Prepaid meters show total energy usage but fail to identify which individual appliances draw the most power.
Unexpected Credit Exhaustion
Users react to high bills or sudden credit depletion after it happens rather than preventing it.
Unaware of Abnormalities
Electrical degradation, wiring issues, or standby power drain go unnoticed due to lack of real-time monitoring.
Background & Problem Statement
Key challenges in household electricity monitoring and tariff management

## Slide 3
IoT Monitoring Nodes
Smart outlets installed at selected power sockets continuously measure Voltage, Current, Power, and Energy.
Central Intelligence Platform
Aggregates data, stores historical records, analyzes consumption patterns, and estimates costs.
Interactive Dashboard
Presents real-time appliance-level and house-level analytics to users.
Proactive Recommendations
Notifies users before reaching higher tariff tiers and flags abnormal electrical behavior.
Proposed IoT Solution
An end-to-end intelligent architecture for domestic energy optimization

## Slide 4
Core Objectives
Develop an intelligent IoT system to monitor, analyze, and optimize household electricity usage.
Target Capabilities
Track V, I, P, E per appliance, estimate daily/monthly cost, predict tariff transitions, and support remote relay control.
Scope Boundaries (Included)
Smart monitoring nodes, cloud/local backend, analytics & recommendation engine, real-time alerts.
Scope Exclusions
Direct integration with official provider meters
certified revenue billing
3-phase industrial systems.
Project Objectives & Scope
Defining system capabilities and boundaries

## Slide 5
Physical Layer
Household appliances, outlets, and electrical wiring.
Sensing Layer
Voltage (V) and Current (I) sensors measuring electrical parameters.
Edge Computing Layer
ESP32 microcontroller performing sampling, power calculations, and MQTT publishing.
Communication Layer
Wi-Fi & MQTT broker transferring JSON data payloads.
Backend & Analytics Layer
Device manager, analytics engine, recommendation engine, and database.
User Intelligence Layer
Interactive Web/Mobile Dashboard for control and insights.
Layered System Architecture
Multi-tier design pattern from physical sensing to user intelligence

## Slide 6
Layered System Architecture

## Slide 7
Microcontroller (ESP32)
Built-in Wi-Fi, dual-core processing, ADC/GPIO interfaces for rapid sensor reading.
Voltage & Current Sensors
Measures instantaneous AC voltage quality and appliance load current.
Relay Control Module
Enables optional remote ON/OFF control and scheduled automated operations.
Power Supply & Status LEDs
Regulates AC to DC power and provides visual Wi-Fi/Relay status indicators.
Hardware Design & Smart Nodes
Component selection for precise edge sampling and safety

## Slide 8
Node-Red Flow Design
Go to Wokwi …

## Slide 9
Publish / Subscribe Model
Lightweight MQTT protocol ensures low bandwidth usage, minimal latency, and high scalability.
Hierarchical Topic Naming
Structured topic tree for scalable message routing:
JSON Data Payload
Transmits nodeId, timestamp, voltage, current, power, energy, and relayState.
Quality of Service (QoS)
QoS 0 for high-frequency measurements; QoS 1 for reliable delivery of control commands and configuration.
Communication Protocol & MQTT
Data telemetry structure and QoS delivery model

## Slide 10
Node-Red Flow Design
Go to Node-red …

## Slide 11
Appliance & House Dashboards
Displays live V, I, P, E, highest-consuming appliance, peak hours, and historical trends.
Tariff & Cost Estimation
Tracks current tariff tier, calculates daily/monthly cost, and predicts next tier jump.
Fault & Anomaly Detection
Flags unusual current spikes, voltage drops, and excessive standby power drain.
Automation & Scheduling
Allows users to set timers, remote ON/OFF rules, and energy-saving schedules.
Software & Intelligent Analytics
User controls, predictive insights, and anomaly detection

## Slide 12
Go to the dashboard …
Software & Intelligent Analytics
User controls, predictive insights, and anomaly detection

## Slide 13
Testing the project …

## Slide 14
Smart Meter Sync
Direct integration with official smart electricity meters for real-time credit syncing.
AI Analytics
Machine learning models for predictive maintenance, load forecasting, and habit learning.
Native Mobile App
Android & iOS apps with push notifications, widgets, and voice assistant integration.
Solar & Renewable Support
Extending system to monitor photovoltaic systems, batteries, and EV chargers.
Future Expansion & Roadmap
Scaling capabilities towards next-generation Home Energy Management Systems

## Slide 15
Key Takeaways:
Actionable Decision Support: Transforms passive energy monitoring into proactive cost reduction and safety management.
Tailored for Egyptian Market: Addresses tier-based tariffs and prepaid meter challenges directly.
Scalable & Modular Architecture: Launches as an IoT prototype while serving as a scalable foundation for full Home Energy Management Systems (HEMS).
Conclusion
Summary of key impacts and project takeaways